## Slide 1: Network+ Guide to Networks 7th Edition
Chapter 5
Network Cabling
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Network+ Guide to Networks 7th Edition
Chapter 5
Network Cabling

## Slide 2: Objectives
Explain basic data transmission concepts, including signaling, data modulation, multiplexing, bandwidth, baseband, and broadband
Describe the physical characteristics and Ethernet standards of coaxial cable, STP, UTP, and fiber-optic media
Compare the benefits and limitations of different networking media
Notes: Objectives
Explain basic data transmission concepts, including signaling, data modulation, multiplexing, bandwidth, baseband, and broadband
Describe the physical characteristics and Ethernet standards of coaxial cable, STP, UTP, and fiber-optic media
Compare the benefits and limitations of different networking media

## Slide 3: Objectives
Explore the connectors, converters, and couplers for each cabling type
Examine common cable problems and differentiate between various tools for troubleshooting those problems
Notes: Objectives
Explore the connectors, converters, and couplers for each cabling type
Examine common cable problems and differentiate between various tools for troubleshooting those problems

## Slide 4: Transmission Basics
Transmission techniques in use on today’s network are complex and varied
This section covers fundamental characteristics that define today’s data transmission
Notes: Transmission Basics
Transmission techniques in use on today’s network are complex and varied
This section covers fundamental characteristics that define today’s data transmission

## Slide 5: Analog Signaling
Analog signals - vary infinitely and continuously
  Appear as a wavy line when graphed over time
Analog signals are characterized by four properties:
  Amplitude
    Measure of strength at given point in time
  Frequency
    Number of times amplitude cycles over fixed time
  Wavelength
    Distance between one peak and the next
  Phase
    Progress of wave over time compared to a fixed point
Notes: Analog Signaling
Analog signals - vary infinitely and continuously
  Appear as a wavy line when graphed over time
Analog signals are characterized by four properties:
  Amplitude
    Measure of strength at given point in time
  Frequency
    Number of times amplitude cycles over fixed time
  Wavelength
    Distance between one peak and the next
  Phase
    Progress of wave over time compared to a fixed point

## Slide 6: Analog Signaling
Notes: Analog Signaling

## Slide 7: Analog Signaling
Drawback of analog signals
  Varied and imprecise voltage
    Susceptible to transmission flaws
Notes: Analog Signaling
Drawback of analog signals
  Varied and imprecise voltage
    Susceptible to transmission flaws

## Slide 8: Digital Signaling
Digital signals
  Pulses of voltages
    Positive voltage represents a 1
    Zero voltage represents a 0
Notes: Digital Signaling
Digital signals
  Pulses of voltages
    Positive voltage represents a 1
    Zero voltage represents a 0

## Slide 9: Digital Signaling
Notes: Digital Signaling

## Slide 10: Data Modulation
Data relies on digital transmission
Network connection may handle only analog signals
Modem
  Accomplishes this translation
  Modulator/demodulator
Data modulation
  Technology modifying analog signals into digital signals and vice versa
  Make analog signals suitable for carrying data over a communication path
Notes: Data Modulation
Data relies on digital transmission
Network connection may handle only analog signals
Modem
  Accomplishes this translation
  Modulator/demodulator
Data modulation
  Technology modifying analog signals into digital signals and vice versa
  Make analog signals suitable for carrying data over a communication path

## Slide 11: Data Modulation
Carrier wave
  Combined with another analog signal
  Produces unique signal
    Transmitted from one node to another
  Preset properties
  Purpose: convey information
Information wave (data wave)
  Added to carrier wave
  Modifies one carrier wave property
Notes: Data Modulation
Carrier wave
  Combined with another analog signal
  Produces unique signal
    Transmitted from one node to another
  Preset properties
  Purpose: convey information
Information wave (data wave)
  Added to carrier wave
  Modifies one carrier wave property

## Slide 12: Data Modulation
Frequency modulation
  Carrier frequency modified by application of data signal
Amplitude modulation
  Carrier signal amplitude modified by application of data signal
Digital subscriber line (DSL)
  Also makes use of modulation
Notes: Data Modulation
Frequency modulation
  Carrier frequency modified by application of data signal
Amplitude modulation
  Carrier signal amplitude modified by application of data signal
Digital subscriber line (DSL)
  Also makes use of modulation

## Slide 13: Data Modulation
Notes: Data Modulation

## Slide 14: Baseband and Broadband
Baseband transmission
  Digital signals that are carried on a single channel
  Requires exclusive use of wire’s capacity
  Example: Ethernet
Broadband transmission
  Multiple transmissions share a single media
  Transmission sharing the same media rely on multiplexing to manage multiple signals
  Example: Cable TV and cable Internet
Notes: Baseband and Broadband
Baseband transmission
  Digital signals that are carried on a single channel
  Requires exclusive use of wire’s capacity
  Example: Ethernet
Broadband transmission
  Multiple transmissions share a single media
  Transmission sharing the same media rely on multiplexing to manage multiple signals
  Example: Cable TV and cable Internet

## Slide 15: Multiplexing
Multiplexing
  A form of transmission that allows multiple signals to travel simultaneously over one medium
Subchannels
  Logical multiple smaller channels
Multiplexer (mux)
  Combines many channel signals
  Required at the transmitting end of the channel
Demultiplexer (demux)
  Separates the combined signals
Notes: Multiplexing
Multiplexing
  A form of transmission that allows multiple signals to travel simultaneously over one medium
Subchannels
  Logical multiple smaller channels
Multiplexer (mux)
  Combines many channel signals
  Required at the transmitting end of the channel
Demultiplexer (demux)
  Separates the combined signals

## Slide 16: Multiplexing
TDM (Time division multiplexing)
  Divides channel into multiple time intervals
Notes: Multiplexing
TDM (Time division multiplexing)
  Divides channel into multiple time intervals

## Slide 17: Multiplexing
Statistical multiplexing
  Transmitter assigns slots to nodes
    According to priority, need
  More efficient than TDM
Notes: Multiplexing
Statistical multiplexing
  Transmitter assigns slots to nodes
    According to priority, need
  More efficient than TDM

## Slide 18: Multiplexing
FDM (Frequency Division Multiplexing)
  Unique frequency band for each communications subchannel
  Cellular telephone transmission
  DSL Internet access
Notes: Multiplexing
FDM (Frequency Division Multiplexing)
  Unique frequency band for each communications subchannel
  Cellular telephone transmission
  DSL Internet access

## Slide 19: Multiplexing
WDM (Wavelength Division Multiplexing)
  One fiber-optic connection
  Carries multiple light signals simultaneously
Notes: Multiplexing
WDM (Wavelength Division Multiplexing)
  One fiber-optic connection
  Carries multiple light signals simultaneously

## Slide 20: Multiplexing
DWDM (Dense Wavelength Division Multiplexing)
  Used on most modern fiber-optic networks
  Extraordinary capacity
  Typically used on high-bandwidth or long-distance WAN links
CWDM (Coarse Wavelength Division Multiplexing)
  Developed after DWDM in an effort to lower the cost of the transceiver equipment needed
  Channels are spaced more widely apart across entire frequency band
Notes: Multiplexing
DWDM (Dense Wavelength Division Multiplexing)
  Used on most modern fiber-optic networks
  Extraordinary capacity
  Typically used on high-bandwidth or long-distance WAN links
CWDM (Coarse Wavelength Division Multiplexing)
  Developed after DWDM in an effort to lower the cost of the transceiver equipment needed
  Channels are spaced more widely apart across entire frequency band

## Slide 21: Throughput and Bandwidth
Throughput
  Amount of data transmitted during given time period
  Also called payload rate or effective data rate
  Expressed as bits transmitted per second
Bandwidth (strict definition)
  Difference between highest and lowest frequencies medium can transmit
  Range of frequencies
Both are commonly expressed as bits transmitted per second, called bit rate
Notes: Throughput and Bandwidth
Throughput
  Amount of data transmitted during given time period
  Also called payload rate or effective data rate
  Expressed as bits transmitted per second
Bandwidth (strict definition)
  Difference between highest and lowest frequencies medium can transmit
  Range of frequencies
Both are commonly expressed as bits transmitted per second, called bit rate

## Slide 22: Throughput and Bandwidth
Notes: Throughput and Bandwidth

## Slide 23: Twisted-Pair Cable
Color-coded insulated copper wire pairs
  0.4 to 0.8 mm diameter
  Encased in a plastic sheath
  Every two wires are twisted
  together
Notes: Twisted-Pair Cable
Color-coded insulated copper wire pairs
  0.4 to 0.8 mm diameter
  Encased in a plastic sheath
  Every two wires are twisted
  together

## Slide 24: Twisted-Pair Cable
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
High twist ratio
  Greater attenuation
Notes: Twisted-Pair Cable
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
High twist ratio
  Greater attenuation

## Slide 25: Twisted-Pair Cable
Hundreds of different designs
  Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Most common twisted pair types
  Category (cat) 3, 5, 5e, 6, 6a, 7
  CAT 5e or higher used in modern LANs
Notes: Twisted-Pair Cable
Hundreds of different designs
  Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Most common twisted pair types
  Category (cat) 3, 5, 5e, 6, 6a, 7
  CAT 5e or higher used in modern LANs

## Slide 26: Twisted-Pair Cable
Advantages
  Relatively inexpensive
  Flexible
  Easy installation
  Spans significant distance before requiring repeater
  Accommodates several different topologies
Two categories
  Shielded twisted pair (STP)
  Unshielded twisted pair (UTP)
Notes: Twisted-Pair Cable
Advantages
  Relatively inexpensive
  Flexible
  Easy installation
  Spans significant distance before requiring repeater
  Accommodates several different topologies
Two categories
  Shielded twisted pair (STP)
  Unshielded twisted pair (UTP)

## Slide 27: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  May be grounded
Notes: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  May be grounded

## Slide 28: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance
Notes: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance

## Slide 29: Comparing STP and UTP
Throughput
  STP and UTP can transmit the same rates
Cost
  STP and UTP vary in cost
Connector
  STP and UTP use Registered Jack 45
Noise immunity
  STP more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters
Notes: Comparing STP and UTP
Throughput
  STP and UTP can transmit the same rates
Cost
  STP and UTP vary in cost
Connector
  STP and UTP use Registered Jack 45
Noise immunity
  STP more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters

## Slide 30: Ethernet Standards for Twisted-Pair Cabling
Notes: Ethernet Standards for Twisted-Pair Cabling

## Slide 31: Cable Pinouts
Proper cable termination is a requirement for two nodes on a network to communicate
TIA/EIA specifies two methods of inserting wires into RJ-45 plugs
  TIA/EIA 568A
  TIA/EIA 568B
No functional difference between the two standards
  Just make sure you use the same standard on every RJ-45 plug and jack
Notes: Cable Pinouts
Proper cable termination is a requirement for two nodes on a network to communicate
TIA/EIA specifies two methods of inserting wires into RJ-45 plugs
  TIA/EIA 568A
  TIA/EIA 568B
No functional difference between the two standards
  Just make sure you use the same standard on every RJ-45 plug and jack

## Slide 32: Cable Pinouts
Notes: Cable Pinouts

## Slide 33: Cable Pinouts
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Rollover cable
  All wires are reversed
  Terminations are a mirror image of each other
  Also called Yost cables or Cisco console cables
  Used to connect a computer to the console port of a router
Notes: Cable Pinouts
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Rollover cable
  All wires are reversed
  Terminations are a mirror image of each other
  Also called Yost cables or Cisco console cables
  Used to connect a computer to the console port of a router

## Slide 34: Copper Connectors and Couplers
Media converter
  Enables networks or segments running on different media to interconnect and exchange signals
Coupler
  Passes data through a homogenous connection without any modification
Notes: Copper Connectors and Couplers
Media converter
  Enables networks or segments running on different media to interconnect and exchange signals
Coupler
  Passes data through a homogenous connection without any modification

## Slide 35: PoE (Power over Ethernet)
PoE - IEEE 802.3af standard which specifies a method for supplying electrical power over twisted-pair Ethernet connections
  Amount of power provided:
    15.4 watts for standard PoE devices
    25.5 watts for newer PoE+ devices (802.3at standard)
PoE standard specifies two types of devices:
  PSE (power sourcing equipment)
  PD (powered devices)
Notes: PoE (Power over Ethernet)
PoE - IEEE 802.3af standard which specifies a method for supplying electrical power over twisted-pair Ethernet connections
  Amount of power provided:
    15.4 watts for standard PoE devices
    25.5 watts for newer PoE+ devices (802.3at standard)
PoE standard specifies two types of devices:
  PSE (power sourcing equipment)
  PD (powered devices)

## Slide 36: PoE (Power over Ethernet)
The IEEE standard requires that a PSE device first determine whether a node is PoE-capable before attempting to supply it with power
On networks that demand PoE but don’t have PoE-capable equipment, you can add PoE adapters
Notes: PoE (Power over Ethernet)
The IEEE standard requires that a PSE device first determine whether a node is PoE-capable before attempting to supply it with power
On networks that demand PoE but don’t have PoE-capable equipment, you can add PoE adapters

## Slide 37: Fiber-Optic Cable
Fiber-optic cable (fiber)
  One or more glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser or light-emitting diode (LED) through central fibers
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend
Notes: Fiber-Optic Cable
Fiber-optic cable (fiber)
  One or more glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser or light-emitting diode (LED) through central fibers
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend

## Slide 38: Fiber-Optic Cable
Plastic buffer outside cladding
  Protects cladding and core
  Opaque to absorb escaping light
  Surrounded by Kevlar (polymeric fiber) strands
Plastic sheath covers Kevlar strands
Notes: Fiber-Optic Cable
Plastic buffer outside cladding
  Protects cladding and core
  Opaque to absorb escaping light
  Surrounded by Kevlar (polymeric fiber) strands
Plastic sheath covers Kevlar strands

## Slide 39: Fiber-Optic Cable
Benefits over copper cabling
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
  Industry standard for high-speed networking
Drawbacks
  More expensive than twisted pair cable
  Requires special equipment to splice
Notes: Fiber-Optic Cable
Benefits over copper cabling
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
  Industry standard for high-speed networking
Drawbacks
  More expensive than twisted pair cable
  Requires special equipment to splice

## Slide 40: Fiber-Optic Cable
Throughput
  Proven reliable in transmitting data at rates that can reach 100 gigabits per second per channel
Cost
  Most expensive transmission medium
Noise immunity
  Unaffected by EMI
Size and scalability
  Segment lengths vary from 150 to 40,000 meters
  Depends on the light’s wavelength and type of cable
Notes: Fiber-Optic Cable
Throughput
  Proven reliable in transmitting data at rates that can reach 100 gigabits per second per channel
Cost
  Most expensive transmission medium
Noise immunity
  Unaffected by EMI
Size and scalability
  Segment lengths vary from 150 to 40,000 meters
  Depends on the light’s wavelength and type of cable

## Slide 41: SMF (Single Mode Fiber)
Consists of narrow core (8-10 microns in diameter)
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating is required
Rarely used for shorter connections
  Due to cost
  The Internet backbone depends on SMF
Notes: SMF (Single Mode Fiber)
Consists of narrow core (8-10 microns in diameter)
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating is required
Rarely used for shorter connections
  Due to cost
  The Internet backbone depends on SMF

## Slide 42: MMF (Multimode Fiber)
Contains a core with a larger diameter than single mode fiber
  Common sizes: 50 or 62.5 microns
Laser or LED generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone
Notes: MMF (Multimode Fiber)
Contains a core with a larger diameter than single mode fiber
  Common sizes: 50 or 62.5 microns
Laser or LED generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone

## Slide 43: Fiber Connectors and Couplers
MMF connectors
  Classified by the number of fibers
SMF connectors
  Classified by size and shape of the ferrule
Ferrule - the extended tip of a connector that makes contact with the receptacle in the jack
Notes: Fiber Connectors and Couplers
MMF connectors
  Classified by the number of fibers
SMF connectors
  Classified by size and shape of the ferrule
Ferrule - the extended tip of a connector that makes contact with the receptacle in the jack

## Slide 44: Fiber Connectors and Couplers
Shapes and polishes used by SMF ferrules to reduce back reflection:
  Physical Contact (PC)
  Ultra Polished Connector (UPC)
  Angle Polished Connector (APC)
Notes: Fiber Connectors and Couplers
Shapes and polishes used by SMF ferrules to reduce back reflection:
  Physical Contact (PC)
  Ultra Polished Connector (UPC)
  Angle Polished Connector (APC)

## Slide 45: Fiber Connectors and Couplers
SMF connectors are typically available with a 1.25-mm ferrule or a 2.5-mm ferrule
  Most common 1.25-mm connector is the LC
  Three 2.5-mm connectors are the SC, ST, and FC
Most common MMF connector is the MT-RJ
Existing fiber networks might use ST or SC connectors
  LC and MT-RJ are used on the very latest fiber-optic technology
Notes: Fiber Connectors and Couplers
SMF connectors are typically available with a 1.25-mm ferrule or a 2.5-mm ferrule
  Most common 1.25-mm connector is the LC
  Three 2.5-mm connectors are the SC, ST, and FC
Most common MMF connector is the MT-RJ
Existing fiber networks might use ST or SC connectors
  LC and MT-RJ are used on the very latest fiber-optic technology

## Slide 46: Fiber-Optic Converters and Modular Interfaces
Converters are required to connect multimode fiber networks to single-mode fiber networks
  Also fiber- and copper-based parts of a network
Bidirectional converter accepts the signal from one part of the network, then regenerates the signal and sends it to the next part of the network
GBIC - a standard type of modular interface designed for Gigabit Ethernet connections
  May contain RJ-45 or fiber-optic cable ports
Notes: Fiber-Optic Converters and Modular Interfaces
Converters are required to connect multimode fiber networks to single-mode fiber networks
  Also fiber- and copper-based parts of a network
Bidirectional converter accepts the signal from one part of the network, then regenerates the signal and sends it to the next part of the network
GBIC - a standard type of modular interface designed for Gigabit Ethernet connections
  May contain RJ-45 or fiber-optic cable ports

## Slide 47: Fiber-Optic Converters and Modular Interfaces
SFP (small form-factor pluggable) transceivers
  Provide the same function as a GBIC, but allow more ports per inch
  Sometimes known as mini GBICs or SFP GBICs
  Two types: XFP and SFP+
Notes: Fiber-Optic Converters and Modular Interfaces
SFP (small form-factor pluggable) transceivers
  Provide the same function as a GBIC, but allow more ports per inch
  Sometimes known as mini GBICs or SFP GBICs
  Two types: XFP and SFP+

## Slide 48: Fiber-Optic Converters and Modular Interfaces
Installing a GBIC or SFP
  Slide the transceiver into a socket on the back of the connectivity device
  Most SFPs come with a tab or latch system and keyed so that they will slide into the socket when aligned properly
Notes: Fiber-Optic Converters and Modular Interfaces
Installing a GBIC or SFP
  Slide the transceiver into a socket on the back of the connectivity device
  Most SFPs come with a tab or latch system and keyed so that they will slide into the socket when aligned properly

## Slide 49: Fiber-Optic Converters and Modular Interfaces
Loopback adapter
  A helpful tool when testing an SFP’s functionality or checking for a mismatch
Notes: Fiber-Optic Converters and Modular Interfaces
Loopback adapter
  A helpful tool when testing an SFP’s functionality or checking for a mismatch

## Slide 50: Ethernet Standards for Fiber-Optic Cable
Notes: Ethernet Standards for Fiber-Optic Cable

## Slide 51: Transmission Flaws
Noise
  Any undesirable influence degrading or distorting signal
Types of noise
  EMI (electromagnetic interference)
    Example: radio frequency interference
  Cross-talk
    Signal on one wire infringes on adjacent wire signal
    Alien cross-talk occurs between two cables
    Near end cross-talk (NEXT) occurs near source
    Far end cross-talk (FEXT) occurs at the far end
Notes: Transmission Flaws
Noise
  Any undesirable influence degrading or distorting signal
Types of noise
  EMI (electromagnetic interference)
    Example: radio frequency interference
  Cross-talk
    Signal on one wire infringes on adjacent wire signal
    Alien cross-talk occurs between two cables
    Near end cross-talk (NEXT) occurs near source
    Far end cross-talk (FEXT) occurs at the far end

## Slide 52: Transmission Flaws
Notes: Transmission Flaws

## Slide 53: Transmission Flaws
Attenuation
  Loss of signal’s strength as it travels away from source
Two ways analog and digital signals are boosted:
  Amplifier - increases the voltage, or strength, of signals
    Can also boot the noise that has accumulated in the signal
  Repeater - regenerates a digital signal in its original form
    Without noise previously accumulated
Notes: Transmission Flaws
Attenuation
  Loss of signal’s strength as it travels away from source
Two ways analog and digital signals are boosted:
  Amplifier - increases the voltage, or strength, of signals
    Can also boot the noise that has accumulated in the signal
  Repeater - regenerates a digital signal in its original form
    Without noise previously accumulated

## Slide 54: Transmission Flaws
Notes: Transmission Flaws

## Slide 55: Transmission Flaws
Latency
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes
  Cable length
  Intervening connectivity device
Round trip time (RTT)
  Time for packet to go from sender to receiver, then back from receiver to sender
Notes: Transmission Flaws
Latency
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes
  Cable length
  Intervening connectivity device
Round trip time (RTT)
  Time for packet to go from sender to receiver, then back from receiver to sender

## Slide 56: Transmission Flaws
Common Fiber Cable Problems:
  Fiber type mismatch
    More of a fiber core mismatch
    Even same-mode cables can be mismatched if the cores have different widths
  Wavelength mismatch
    SMF, MMF, and POF (Plastic Optical Fiber) use different wavelengths
  Dirty connectors
    Signal loss and other errors can start to cause problems
Notes: Transmission Flaws
Common Fiber Cable Problems:
  Fiber type mismatch
    More of a fiber core mismatch
    Even same-mode cables can be mismatched if the cores have different widths
  Wavelength mismatch
    SMF, MMF, and POF (Plastic Optical Fiber) use different wavelengths
  Dirty connectors
    Signal loss and other errors can start to cause problems

## Slide 57: Troubleshooting Tools
Tone generator (toner)
  Small electronic device
  Issues signal on wire pair
Tone locator (probe)
  Emits tone when electrical activity detected
Probe kit or toner probe
  Generator and locator combination
Testing requires trial and error
Used to determine where wired pair terminates
Not used to determine cable characteristics
Notes: Troubleshooting Tools
Tone generator (toner)
  Small electronic device
  Issues signal on wire pair
Tone locator (probe)
  Emits tone when electrical activity detected
Probe kit or toner probe
  Generator and locator combination
Testing requires trial and error
Used to determine where wired pair terminates
Not used to determine cable characteristics

## Slide 58: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 59: Troubleshooting Tools
Multimeter
  Measures electric circuit characteristics
    Resistance, voltage, and impedance
Use a multimeter to do the following:
  Measure voltage to verify cable is conducting electricity
  Check for the presence of noise
  Verify the amount of resistance is appropriate
  Test for short or open circuits in the wire
Notes: Troubleshooting Tools
Multimeter
  Measures electric circuit characteristics
    Resistance, voltage, and impedance
Use a multimeter to do the following:
  Measure voltage to verify cable is conducting electricity
  Check for the presence of noise
  Verify the amount of resistance is appropriate
  Test for short or open circuits in the wire

## Slide 60: Troubleshooting Tools
Cable continuity testers (cable testers)
  Tests whether cable carries signal to destination
Copper-based cable tester
  Consists of two parts
    Base unit generates voltage
    Remote unit detects voltage
Series of lights, audible tone
  Used to signal pass/fail
Notes: Troubleshooting Tools
Cable continuity testers (cable testers)
  Tests whether cable carries signal to destination
Copper-based cable tester
  Consists of two parts
    Base unit generates voltage
    Remote unit detects voltage
Series of lights, audible tone
  Used to signal pass/fail

## Slide 61: Troubleshooting Tools
Some continuity testers verify UTP, STP wires paired correctly
  Not shorted, exposed, crossed
Fiber optic continuity tester
  Issues light pulses on fiber
  Determines whether pulses reach other end
Test all cables to ensure meeting network’s required standards
  Homemade or purchased
Offer convenience: portable, lightweight, low cost
Notes: Troubleshooting Tools
Some continuity testers verify UTP, STP wires paired correctly
  Not shorted, exposed, crossed
Fiber optic continuity tester
  Issues light pulses on fiber
  Determines whether pulses reach other end
Test all cables to ensure meeting network’s required standards
  Homemade or purchased
Offer convenience: portable, lightweight, low cost

## Slide 62: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 63: Troubleshooting Tools
Cable performance tester, line tester, or certifier
  Performs similarly to continuity testers but can be used to:
    Measure distance to a connectivity device, termination point, or cable fault
    Measure attenuation
    Measure near end cross-talk
    Measure termination resistance and impedance
    Issue pass/fail ratings for Cat 3-7 standards
    Store and print results or save to a computer database
    Graphically depict attenuation and cross-talk
Notes: Troubleshooting Tools
Cable performance tester, line tester, or certifier
  Performs similarly to continuity testers but can be used to:
    Measure distance to a connectivity device, termination point, or cable fault
    Measure attenuation
    Measure near end cross-talk
    Measure termination resistance and impedance
    Issue pass/fail ratings for Cat 3-7 standards
    Store and print results or save to a computer database
    Graphically depict attenuation and cross-talk
Cable performance tester, line tester, or certifier
  Performs similarly to continuity testers but can be used to:
    Measure distance to a connectivity device, termination point, or cable fault
    Measure attenuation
    Measure near end cross-talk
    Measure termination resistance and impedance
    Issue pass/fail ratings for Cat 3-7 standards
    Store and print results or save to a computer database
    Graphically depict attenuation and cross-talk

## Slide 64: Troubleshooting Tools
TDR (time domain reflectometer)
  Issue signal, measures signal bounce back
  Indicates distance between nodes
  Indicates whether terminators properly installed, functional
OTDRs (optical time domain reflectometers)
  Measure fiber length
  Determine faulty splice locations, breaks, connectors, bends and measure attenuation over cable
  Expensive
Notes: Troubleshooting Tools
TDR (time domain reflectometer)
  Issue signal, measures signal bounce back
  Indicates distance between nodes
  Indicates whether terminators properly installed, functional
OTDRs (optical time domain reflectometers)
  Measure fiber length
  Determine faulty splice locations, breaks, connectors, bends and measure attenuation over cable
  Expensive

## Slide 65: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 66: Troubleshooting Tools
OPM (Optical Power Meter)
  Also called a laser power meter or a light meter
  Measures the amount of light power transmitted on a fiber-optic line
  Must be calibrated precisely following highly accurate optical power standards
  Surrounding room temperature, connection type, and the skill of the technician all affect the final test results
Notes: Troubleshooting Tools
OPM (Optical Power Meter)
  Also called a laser power meter or a light meter
  Measures the amount of light power transmitted on a fiber-optic line
  Must be calibrated precisely following highly accurate optical power standards
  Surrounding room temperature, connection type, and the skill of the technician all affect the final test results

## Slide 67: Summary
Computers generate and interpret data signals as electrical current where voltage is finitely measured as on or off and interpreted as binary data
A channel is a distinct communication path between nodes and may be separated logically or physically
A baseband transmission is the only transmission on the media, in broadband, multiple transmissions share a single media
  Broadband transmission require multiplexing
Throughput is the measure of how much data is transmitted during a given time period
Notes: Summary
Computers generate and interpret data signals as electrical current where voltage is finitely measured as on or off and interpreted as binary data
A channel is a distinct communication path between nodes and may be separated logically or physically
A baseband transmission is the only transmission on the media, in broadband, multiple transmissions share a single media
  Broadband transmission require multiplexing
Throughput is the measure of how much data is transmitted during a given time period

## Slide 68: Summary
Coaxial cable was the foundation for Ethernet networks in the 1980s
Twisted-pair cable consists of color-coded pairs of insulated copper wires that are twisted in pairs
STP cable consists of twisted-pair wires that are not only individually insulated, but also surrounded by a shielding made of a metallic substance
UTP does not contain additional shielding
TIA/EIA has specified two different methods of inserting wires into RJ-45 plugs: 568A and 568B
Notes: Summary
Coaxial cable was the foundation for Ethernet networks in the 1980s
Twisted-pair cable consists of color-coded pairs of insulated copper wires that are twisted in pairs
STP cable consists of twisted-pair wires that are not only individually insulated, but also surrounded by a shielding made of a metallic substance
UTP does not contain additional shielding
TIA/EIA has specified two different methods of inserting wires into RJ-45 plugs: 568A and 568B

## Slide 69: Summary
A rollover cable uses a reverse image of the pinout of the other end of a cable
Fiber-optic cable contains one or more several glass or plastic fibers at it core
SMF accommodates the highest bandwidths and longest distances of all network transmission media
MMF contains a core with a larger diameter
Fiber-optic cabling is the best medium for delivering high throughput
A common source of noise is EMI
Notes: Summary
A rollover cable uses a reverse image of the pinout of the other end of a cable
Fiber-optic cable contains one or more several glass or plastic fibers at it core
SMF accommodates the highest bandwidths and longest distances of all network transmission media
MMF contains a core with a larger diameter
Fiber-optic cabling is the best medium for delivering high throughput
A common source of noise is EMI

## Slide 70: Summary
Cross-talk occurs when a signal traveling on one wire or cable infringes on the signal traveling on an adjacent wire or cable
Attenuation is the loss of a signal’s strength
Latency is the delay between the instant data leaves the source and when it arrives at its destination
A multimeter is a simple instrument that measures resistance, voltage, impedance, and other characteristics
Tools used to test cables: cable checkers, continuity testers, cable testers, and light meters (for fiber)
Notes: Summary
Cross-talk occurs when a signal traveling on one wire or cable infringes on the signal traveling on an adjacent wire or cable
Attenuation is the loss of a signal’s strength
Latency is the delay between the instant data leaves the source and when it arrives at its destination
A multimeter is a simple instrument that measures resistance, voltage, impedance, and other characteristics
Tools used to test cables: cable checkers, continuity testers, cable testers, and light meters (for fiber)