## Slide 1: Network+ Guide to Networks 7th Edition
Chapter 9
Unified Communications and Network Performance Management
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Network+ Guide to Networks 7th Edition
Chapter 9
Unified Communications and Network Performance Management

## Slide 2: Objectives
Describe the basic concepts of network management
Utilize system and event logs to evaluate, monitor, and manage network performance
Explain how unified communications, including voice and video transmissions, affect network performance
Explain three common quality of service techniques
Troubleshoot network availability issues and evaluate network redundancy measures
Notes: Objectives
Describe the basic concepts of network management
Utilize system and event logs to evaluate, monitor, and manage network performance
Explain how unified communications, including voice and video transmissions, affect network performance
Explain three common quality of service techniques
Troubleshoot network availability issues and evaluate network redundancy measures

## Slide 3: Fundamentals of Network Management
Network management
  Assess, monitor, and maintain all network aspects
  Scope differs according to network’s size and importance
  Several network management disciplines
  All share same goals
    Enhance efficiency and performance
    Prevent costly downtime and loss
  Predict problems before they occur
Notes: Fundamentals of Network Management
Network management
  Assess, monitor, and maintain all network aspects
  Scope differs according to network’s size and importance
  Several network management disciplines
  All share same goals
    Enhance efficiency and performance
    Prevent costly downtime and loss
  Predict problems before they occur

## Slide 4: Baseline Measurements
Baseline
  Report of network’s current operation state
Example baseline measurements
  Network backbone utilization rate
  Number of users logged on per day or per hour
  Number of protocols running on network
  Error statistics
    Runts, jabbers, or giants
  Frequency of application use
  Bandwidth usage
Notes: Baseline Measurements
Baseline
  Report of network’s current operation state
Example baseline measurements
  Network backbone utilization rate
  Number of users logged on per day or per hour
  Number of protocols running on network
  Error statistics
    Runts, jabbers, or giants
  Frequency of application use
  Bandwidth usage

## Slide 5: Baseline Measurements
Notes: Baseline Measurements

## Slide 6: Baseline Measurements
Compare future and past performance
  Most critical network, user functions
  More data provides more accuracy
Forecasting network traffic patterns
  Difficult to predict users’ habits, new technology effects, changes in resource demand
Gathering baseline data
  Software applications
    Freeware
    Expensive, customizable hardware and software
Notes: Baseline Measurements
Compare future and past performance
  Most critical network, user functions
  More data provides more accuracy
Forecasting network traffic patterns
  Difficult to predict users’ habits, new technology effects, changes in resource demand
Gathering baseline data
  Software applications
    Freeware
    Expensive, customizable hardware and software

## Slide 7: Policies, Procedures, and Regulations
Rules limit chaos, confusion, and downtime
State and federal regulations
  CALEA (Communications Assistance for Law Enforcement Act)
    Telecommunications carriers, equipment manufacturers must provide for surveillance capabilities
  HIPAA (Health Insurance Portability and Accountability Act)
    Protect medical records security and privacy
Notes: Policies, Procedures, and Regulations
Rules limit chaos, confusion, and downtime
State and federal regulations
  CALEA (Communications Assistance for Law Enforcement Act)
    Telecommunications carriers, equipment manufacturers must provide for surveillance capabilities
  HIPAA (Health Insurance Portability and Accountability Act)
    Protect medical records security and privacy

## Slide 8: Policies, Procedures, and Regulations
PCI DSS (Payment Card Industry Data Security Standard)
  Created by the PCI Security Standards Council
  To protect credit card data and transactions
  Requires network segmentation as part of security controls
Many policies and procedures
  Are not laws, but are best practices to prevent network problems
Notes: Policies, Procedures, and Regulations
PCI DSS (Payment Card Industry Data Security Standard)
  Created by the PCI Security Standards Council
  To protect credit card data and transactions
  Requires network segmentation as part of security controls
Many policies and procedures
  Are not laws, but are best practices to prevent network problems

## Slide 9: Monitoring and Managing Network Traffic
Assess network’s status on an ongoing basis
Performance management
  Monitor links and devices’ ability to keep up with demand
Fault management
  Detection and signaling of device, link, component faults
Notes: Monitoring and Managing Network Traffic
Assess network’s status on an ongoing basis
Performance management
  Monitor links and devices’ ability to keep up with demand
Fault management
  Detection and signaling of device, link, component faults

## Slide 10: SNMP Logs
Enterprise-wide network management systems
  Accomplish fault and performance management
  All use similar architecture
Central collection point is called the network management system (NMS)
  Network management agent
    Software routine that collects information about device’s operation
    Provides information to the NMS
  Managed device
    Any network node monitored by the NMS
Notes: SNMP Logs
Enterprise-wide network management systems
  Accomplish fault and performance management
  All use similar architecture
Central collection point is called the network management system (NMS)
  Network management agent
    Software routine that collects information about device’s operation
    Provides information to the NMS
  Managed device
    Any network node monitored by the NMS

## Slide 11: SNMP Logs
Various aspects of a device can be managed
  Processor, memory, hard disk, NIC, and intangibles
MIB (Management Information Base)
  Contains managed devices definition, data
SNMP (Simple Network Management Protocol)
  Used to communicate managed device information
  Part of TCP/IP suite
  SNMPv3: most secure version of the protocol
  SNMPv2: still widely used
  SNMPv1: original version; rarely used today
Notes: SNMP Logs
Various aspects of a device can be managed
  Processor, memory, hard disk, NIC, and intangibles
MIB (Management Information Base)
  Contains managed devices definition, data
SNMP (Simple Network Management Protocol)
  Used to communicate managed device information
  Part of TCP/IP suite
  SNMPv3: most secure version of the protocol
  SNMPv2: still widely used
  SNMPv1: original version; rarely used today

## Slide 12: SNMP Logs
Notes: SNMP Logs

## Slide 13: SNMP Logs
Several ways to view and analyze data
Network management applications
  Flexible
  Challenging to configure and fine-tune
  Choose correct type and amount of information to collect
Notes: SNMP Logs
Several ways to view and analyze data
Network management applications
  Flexible
  Challenging to configure and fine-tune
  Choose correct type and amount of information to collect

## Slide 14: System and Event Logs
Log
  Contains recorded conditions recognized by operating system
Event log
  Windows-based computer log containing monitored device information
Event Viewer application
  Application to view log information in Windows
Notes: System and Event Logs
Log
  Contains recorded conditions recognized by operating system
Event log
  Windows-based computer log containing monitored device information
Event Viewer application
  Application to view log information in Windows

## Slide 15: System and Event Logs
Syslog function
  Standard for generating, storing, and processing messages about events on Linux or UNIX
  Data written to system log
Syslog defines roles for each computer that participates in logging
  Generator - computer that is monitored by a syslog-compatible application and issues event information
  Collector - computer that gathers event messages from generators
Notes: System and Event Logs
Syslog function
  Standard for generating, storing, and processing messages about events on Linux or UNIX
  Data written to system log
Syslog defines roles for each computer that participates in logging
  Generator - computer that is monitored by a syslog-compatible application and issues event information
  Collector - computer that gathers event messages from generators

## Slide 16: System and Event Logs
Using logs for fault management
  Logs keep history
  Information collected does not point to problem
  Logs must be monitored for errors
  Most UNIX and Linux OSs provide a GUI application used for viewing and filtering information
Notes: System and Event Logs
Using logs for fault management
  Logs keep history
  Information collected does not point to problem
  Logs must be monitored for errors
  Most UNIX and Linux OSs provide a GUI application used for viewing and filtering information

## Slide 17: Traffic Analysis
Network monitor
  Tool that continually monitors network traffic
Interface monitor
  Tool that can monitor traffic at a specific interface between a server or client and the network
Difference
  Network monitor can monitor traffic that a single device encounters
  Interface monitor can monitor traffic patterns throughout a particular network
Notes: Traffic Analysis
Network monitor
  Tool that continually monitors network traffic
Interface monitor
  Tool that can monitor traffic at a specific interface between a server or client and the network
Difference
  Network monitor can monitor traffic that a single device encounters
  Interface monitor can monitor traffic patterns throughout a particular network

## Slide 18: Traffic Analysis
Notes: Traffic Analysis

## Slide 19: Traffic Analysis
All network monitoring tools can perform the following functions:
  Set the NIC to run in promiscuous mode to pass all traffic to the monitoring software
  Continuously monitor network traffic on a segment
  Capture network data transmitted on a segment
  Capture frames sent to or from a specific node
  Reproduce network conditions by transmitting a selected amount and type of data
  Generate statistics about network activity
Notes: Traffic Analysis
All network monitoring tools can perform the following functions:
  Set the NIC to run in promiscuous mode to pass all traffic to the monitoring software
  Continuously monitor network traffic on a segment
  Capture network data transmitted on a segment
  Capture frames sent to or from a specific node
  Reproduce network conditions by transmitting a selected amount and type of data
  Generate statistics about network activity

## Slide 20: Traffic Analysis
Some network monitoring tools can also perform the following functions:
  Discover all network nodes on a segment
  Establish a baseline, including performance, utilization rate, and so on
  Track utilization of network resources and device resources and report it in graphs or charts
  Store traffic data and generate reports
  Trigger alarms for certain preconfigured conditions
  Identify usage anomalies, such as top talkers or top listeners
Notes: Traffic Analysis
Some network monitoring tools can also perform the following functions:
  Discover all network nodes on a segment
  Establish a baseline, including performance, utilization rate, and so on
  Track utilization of network resources and device resources and report it in graphs or charts
  Store traffic data and generate reports
  Trigger alarms for certain preconfigured conditions
  Identify usage anomalies, such as top talkers or top listeners

## Slide 21: Traffic Analysis
Monitoring tools can help identify the following:
  Runts
  Giants
  Jabber
  Ghosts
  Packet loss
  Discarded packets
  Interface resets
Alerts might be transmitted by email or text
  Called SMS (Short Message Service)
Notes: Traffic Analysis
Monitoring tools can help identify the following:
  Runts
  Giants
  Jabber
  Ghosts
  Packet loss
  Discarded packets
  Interface resets
Alerts might be transmitted by email or text
  Called SMS (Short Message Service)

## Slide 22: Traffic Management
Traffic shaping (packet shaping)
  Manipulating packet, data stream, and connection characteristics
    Manage type and amount of traffic traversing network
  Goals
    Assure timely delivery of most important traffic
    Offer best possible performance for all users
Notes: Traffic Management
Traffic shaping (packet shaping)
  Manipulating packet, data stream, and connection characteristics
    Manage type and amount of traffic traversing network
  Goals
    Assure timely delivery of most important traffic
    Offer best possible performance for all users

## Slide 23: Traffic Management
Techniques
  Delay less important traffic
  Increase priority of more important traffic
  Traffic policing
    Limit traffic volume flowing in and out of interface during specified time period
    Limit momentary throughput rate for an interface
Not without controversy
  Comcast discriminated against certain traffic types
Notes: Traffic Management
Techniques
  Delay less important traffic
  Increase priority of more important traffic
  Traffic policing
    Limit traffic volume flowing in and out of interface during specified time period
    Limit momentary throughput rate for an interface
Not without controversy
  Comcast discriminated against certain traffic types

## Slide 24: Traffic Management
Traffic prioritization
  Treating more important traffic preferentially
Prioritization based on characteristics
  Protocol
  IP address
  User group
  DiffServ (Differentiated Services) flag in an IP packet
  VLAN tag in Data Link layer frame
  Service or application
Notes: Traffic Management
Traffic prioritization
  Treating more important traffic preferentially
Prioritization based on characteristics
  Protocol
  IP address
  User group
  DiffServ (Differentiated Services) flag in an IP packet
  VLAN tag in Data Link layer frame
  Service or application

## Slide 25: Caching
Caching
  Local storage of frequently needed files
  Allows quick access
Web caching
  Most common caching type, highly customizable
  Web pages stored locally
    On host or network, and then delivered to requesters
ISP cache engine
  Network device devoted to storage, frequently requested file delivery
  Saves money; lowers WAN traffic
Notes: Caching
Caching
  Local storage of frequently needed files
  Allows quick access
Web caching
  Most common caching type, highly customizable
  Web pages stored locally
    On host or network, and then delivered to requesters
ISP cache engine
  Network device devoted to storage, frequently requested file delivery
  Saves money; lowers WAN traffic

## Slide 26: Unified Communications Technologies
PSTN (Public Switched Telephone Network)
  Circuit-switched model, carries telephone calls/faxes
Switching
  Determines how connections are created between nodes
Circuit-switched networks
  Connection is established between two network nodes before transmitting data
Packet-switched networks
  Break data into packets before they are transported
Notes: Unified Communications Technologies
PSTN (Public Switched Telephone Network)
  Circuit-switched model, carries telephone calls/faxes
Switching
  Determines how connections are created between nodes
Circuit-switched networks
  Connection is established between two network nodes before transmitting data
Packet-switched networks
  Break data into packets before they are transported

## Slide 27: Unified Communications Technologies
Greatest advantage to packet switching
  Does not waste bandwidth by holding a connection open until a message reaches its destination
Ethernet networks and the Internet
  Most common examples of packet-switched networks
In unified communications, a user can:
  Access the Web
  Send/receive faxes, email, voice mail, instant messages, or telephone calls
  Participate in videoconference calls
Notes: Unified Communications Technologies
Greatest advantage to packet switching
  Does not waste bandwidth by holding a connection open until a message reaches its destination
Ethernet networks and the Internet
  Most common examples of packet-switched networks
In unified communications, a user can:
  Access the Web
  Send/receive faxes, email, voice mail, instant messages, or telephone calls
  Participate in videoconference calls

## Slide 28: VoIP Applications and Interfaces
IP telephony (VoIP)
  Any network carrying voice signals using TCP/IP
    Public or private
  Runs over any packet-switched network
Data connection types carrying VoIP signals
  T-carriers, ISDN, DSL, broadband cable, satellite connections, WiFi, WiMAX, HSPA+, LTE, cellular telephone networks
Notes: VoIP Applications and Interfaces
IP telephony (VoIP)
  Any network carrying voice signals using TCP/IP
    Public or private
  Runs over any packet-switched network
Data connection types carrying VoIP signals
  T-carriers, ISDN, DSL, broadband cable, satellite connections, WiFi, WiMAX, HSPA+, LTE, cellular telephone networks

## Slide 29: VoIP Applications and Interfaces
Reasons for implementing VoIP
  Lower voice call cost
  New, enhanced features and applications
  Centralize voice and data network management
Voice and data configurations
  Analog telephone (sends, receives analog signals) and must be connected to one of the following:
    ATA analog telephone adapter
    Switch, router, or gateway capable of accepting analog signals and convert them into packets
    Digital PBX (IP-PBX) or analog PBX
Notes: VoIP Applications and Interfaces
Reasons for implementing VoIP
  Lower voice call cost
  New, enhanced features and applications
  Centralize voice and data network management
Voice and data configurations
  Analog telephone (sends, receives analog signals) and must be connected to one of the following:
    ATA analog telephone adapter
    Switch, router, or gateway capable of accepting analog signals and convert them into packets
    Digital PBX (IP-PBX) or analog PBX

## Slide 30: VoIP Applications and Interfaces
Voice and data configurations (cont’d)
  IP telephones
    Transmit and receive only digital signals
  Softphones
    A computer programed to act like an IP phone
Notes: VoIP Applications and Interfaces
Voice and data configurations (cont’d)
  IP telephones
    Transmit and receive only digital signals
  Softphones
    A computer programed to act like an IP phone

## Slide 31: VoIP Applications and Interfaces
Notes: VoIP Applications and Interfaces

## Slide 32: Video over IP Applications and Interfaces
Videoconferencing (video teleconferencing or VTC)
  Allows multiple participants to communicate and collaborate in a real-time meeting
Cisco Systems estimate
  By 2018, over 79% of Internet traffic will be video traffic
Factors fueling growth
  Large quantity of video content available
  Increasing number of devices accessing Internet
  Decreasing cost of bandwidth and equipment
Notes: Video over IP Applications and Interfaces
Videoconferencing (video teleconferencing or VTC)
  Allows multiple participants to communicate and collaborate in a real-time meeting
Cisco Systems estimate
  By 2018, over 79% of Internet traffic will be video traffic
Factors fueling growth
  Large quantity of video content available
  Increasing number of devices accessing Internet
  Decreasing cost of bandwidth and equipment

## Slide 33: Streaming Video
Simplest among video-over-IP applications
  Basic computer hardware, software requirements
Video-on-demand (VoD)
  Files stored on video streaming server
  Popular
  Viewer chooses video when convenient
    Views using Web browser
Live streaming video
  From source directly to user
Notes: Streaming Video
Simplest among video-over-IP applications
  Basic computer hardware, software requirements
Video-on-demand (VoD)
  Files stored on video streaming server
  Popular
  Viewer chooses video when convenient
    Views using Web browser
Live streaming video
  From source directly to user

## Slide 34: Streaming Video
Notes: Streaming Video

## Slide 35: Streaming Video
Consider number of clients receiving each service
  Point-to-point video over IP
  Point-to-multipoint video over IP
    Not the same as multicast transmission
Unicast transmissions
  Single node issues data stream to one other node
  Example: CSPAN source issues signals to each viewer
Network classification: public or private
  Most streaming video occurs over public networks
Notes: Streaming Video
Consider number of clients receiving each service
  Point-to-point video over IP
  Point-to-multipoint video over IP
    Not the same as multicast transmission
Unicast transmissions
  Single node issues data stream to one other node
  Example: CSPAN source issues signals to each viewer
Network classification: public or private
  Most streaming video occurs over public networks

## Slide 36: Videoconferencing
Unidirectional video-over-IP services
  Video delivered to user who only watches content
Videoconferencing
  Full-duplex connections
    Participants send and receive audiovisual signals
  Real time
  Benefits
    Cost savings, convenience
    Replace face-to-face business meetings
    Allow collaboration
Notes: Videoconferencing
Unidirectional video-over-IP services
  Video delivered to user who only watches content
Videoconferencing
  Full-duplex connections
    Participants send and receive audiovisual signals
  Real time
  Benefits
    Cost savings, convenience
    Replace face-to-face business meetings
    Allow collaboration

## Slide 37: Videoconferencing
Videoconferencing uses
  Telemedicine
  Tele-education
  Judicial proceedings
  Surveillance
Hardware, software requirements
  A means to generate, send and receive audiovisual signals
    Computer workstation with cameras, microphones, software
    Video terminal or video phone
Notes: Videoconferencing
Videoconferencing uses
  Telemedicine
  Tele-education
  Judicial proceedings
  Surveillance
Hardware, software requirements
  A means to generate, send and receive audiovisual signals
    Computer workstation with cameras, microphones, software
    Video terminal or video phone

## Slide 38: Videoconferencing
Notes: Videoconferencing

## Slide 39: Videoconferencing
Video bridge
  Manages multiple audiovisual sessions
    Participants can see, hear each other
  Conference server
    Hardware or software
Leased Internet-accessible video bridging services
  For occasional videoconference use
Video bridges depend on signaling protocols
Notes: Videoconferencing
Video bridge
  Manages multiple audiovisual sessions
    Participants can see, hear each other
  Conference server
    Hardware or software
Leased Internet-accessible video bridging services
  For occasional videoconference use
Video bridges depend on signaling protocols

## Slide 40: Signaling Protocols
Signaling
  Information exchange between network components or system
  Establish, monitor, and release connections
  Control system operations
Signaling protocols
  Set up, manage client sessions
  Perform several other functions
Early VoIP: vendors developed proprietary signaling protocols
Today: standardized signaling protocols are used
Notes: Signaling Protocols
Signaling
  Information exchange between network components or system
  Establish, monitor, and release connections
  Control system operations
Signaling protocols
  Set up, manage client sessions
  Perform several other functions
Early VoIP: vendors developed proprietary signaling protocols
Today: standardized signaling protocols are used

## Slide 41: H.323
ITU standard describing architecture, protocols
  Establishing, managing packet-switched network multimedia sessions
Supports voice, video-over-IP services
Terms
  H.323 terminal
  H.323 gateway
  H.323 gatekeeper
  MCU (multipoint control unit)
  H.323 zone
Notes: H.323
ITU standard describing architecture, protocols
  Establishing, managing packet-switched network multimedia sessions
Supports voice, video-over-IP services
Terms
  H.323 terminal
  H.323 gateway
  H.323 gatekeeper
  MCU (multipoint control unit)
  H.323 zone

## Slide 42: H.323
Notes: H.323

## Slide 43: H.323
H.225 and H.245 signaling protocols
  Specified in H.323 standard
  Operate at Session layer
H.225 handles call or videoconference signaling
H.245 ensures correct information type formatting
  Uses logical channels
H.323 standard
  Specifies protocol interoperability
    Presentation layer: coding, decoding signals
    Transport layer
Notes: H.323
H.225 and H.245 signaling protocols
  Specified in H.323 standard
  Operate at Session layer
H.225 handles call or videoconference signaling
H.245 ensures correct information type formatting
  Uses logical channels
H.323 standard
  Specifies protocol interoperability
    Presentation layer: coding, decoding signals
    Transport layer

## Slide 44: SIP (Session Initiation Protocol)
Application layer signaling, multiservice control protocol, packet-based networks
  Performs similar functions as H.323
Modeled on HTTP
Reuse existing TCP/IP protocols
  Session management, enhanced services
Modular and specific
Limited capabilities compared to H.323
  Example: no caller ID
Notes: SIP (Session Initiation Protocol)
Application layer signaling, multiservice control protocol, packet-based networks
  Performs similar functions as H.323
Modeled on HTTP
Reuse existing TCP/IP protocols
  Session management, enhanced services
Modular and specific
Limited capabilities compared to H.323
  Example: no caller ID

## Slide 45: SIP (Session Initiation Protocol)
SIP network components
  User agent
  User agent client
  User agent server
  Registrar server
  Proxy server
  Redirect server
Notes: SIP (Session Initiation Protocol)
SIP network components
  User agent
  User agent client
  User agent server
  Registrar server
  Proxy server
  Redirect server

## Slide 46: SIP (Session Initiation Protocol)
Notes: SIP (Session Initiation Protocol)

## Slide 47: SIP (Session Initiation Protocol)
Advantages of SIP over H.323
  Simplicity
  Fewer instructions to control call
  Consumes fewer processing resources
  More flexible
SIP and H.323
  Regulate call signaling, control for VoIP or video-over-IP clients and servers
  Do not account for communication between media gateways
Notes: SIP (Session Initiation Protocol)
Advantages of SIP over H.323
  Simplicity
  Fewer instructions to control call
  Consumes fewer processing resources
  More flexible
SIP and H.323
  Regulate call signaling, control for VoIP or video-over-IP clients and servers
  Do not account for communication between media gateways

## Slide 48: MGCP (Media Gateway Control Protocol) and Megaco (H.248)
Media gateway (UC Gateway)
  Accepts PSTN lines
  Converts analog signals into VoIP format
  Translates between different signaling protocols
Information transmissions use different channels than control signals
  Also different logical and physical paths
  Expedites information handling
Gateways still need to exchange and translate signaling and control information
Notes: MGCP (Media Gateway Control Protocol) and Megaco (H.248)
Media gateway (UC Gateway)
  Accepts PSTN lines
  Converts analog signals into VoIP format
  Translates between different signaling protocols
Information transmissions use different channels than control signals
  Also different logical and physical paths
  Expedites information handling
Gateways still need to exchange and translate signaling and control information

## Slide 49: MGCP (Media Gateway Control Protocol) and Megaco (H.248)
MGC (media gateway controller)
  Computer managing multiple media gateways
  Facilitates exchange of call signaling information
  Also called a softswitch
  Advantageous on large VoIP networks
MGCP (Media Gateway Control Protocol)
  Used on multiservice networks supporting many media gateways
  Operate with H.323 or SIP
  Older protocol
Notes: MGCP (Media Gateway Control Protocol) and Megaco (H.248)
MGC (media gateway controller)
  Computer managing multiple media gateways
  Facilitates exchange of call signaling information
  Also called a softswitch
  Advantageous on large VoIP networks
MGCP (Media Gateway Control Protocol)
  Used on multiservice networks supporting many media gateways
  Operate with H.323 or SIP
  Older protocol

## Slide 50: MGCP (Media Gateway Control Protocol) and Megaco (H.248)
Notes: MGCP (Media Gateway Control Protocol) and Megaco (H.248)

## Slide 51: MGCP (Media Gateway Control Protocol) and Megaco (H.248)
MEGACO
  Newer protocol
  Performs same functions as MGC
  Different commands and processes
  Operates with H.323 or SIP
  Superior to MGCP
  Supports ATM
  Developed by ITU and IETF
Notes: MGCP (Media Gateway Control Protocol) and Megaco (H.248)
MEGACO
  Newer protocol
  Performs same functions as MGC
  Different commands and processes
  Operates with H.323 or SIP
  Superior to MGCP
  Supports ATM
  Developed by ITU and IETF

## Slide 52: Transport Protocols
A different protocol set delivers voice or video payload
  Transport layer
Transport layer protocols
  TCP: connection oriented protocol
    Delivery guarantees
  UDP: connectionless protocol
    No accountability; preferred for real-time applications
    Packet loss tolerable if additional protocols overcome UDP shortcomings
Notes: Transport Protocols
A different protocol set delivers voice or video payload
  Transport layer
Transport layer protocols
  TCP: connection oriented protocol
    Delivery guarantees
  UDP: connectionless protocol
    No accountability; preferred for real-time applications
    Packet loss tolerable if additional protocols overcome UDP shortcomings

## Slide 53: RTP (Real-time Transport Protocol)
Operates at Application layer
Relies on UDP at the Transport layer
Applies sequence numbers to indicate:
  Destination packet assembly order
  Packet loss during transmission
Assigns packet timestamp
  Receiving node
  Compensates for network delay
  Synchronizes signals
No mechanism to detect success
Notes: RTP (Real-time Transport Protocol)
Operates at Application layer
Relies on UDP at the Transport layer
Applies sequence numbers to indicate:
  Destination packet assembly order
  Packet loss during transmission
Assigns packet timestamp
  Receiving node
  Compensates for network delay
  Synchronizes signals
No mechanism to detect success

## Slide 54: RTCP (Real-time Transport Control Protocol)
Provides quality feedback to participants
  Packets transmitted periodically
  RTCP allows for several message types
RTCP value
  Depends on clients’, applications’ information use
Not mandatory on RTP networks
RTP and RTCP
  Provide information about packet order, loss, delay
  Cannot correct transmission flaws
Notes: RTCP (Real-time Transport Control Protocol)
Provides quality feedback to participants
  Packets transmitted periodically
  RTCP allows for several message types
RTCP value
  Depends on clients’, applications’ information use
Not mandatory on RTP networks
RTP and RTCP
  Provide information about packet order, loss, delay
  Cannot correct transmission flaws

## Slide 55: QoS (Quality of Service) Assurance
VoIP, video over IP transmission difficulty
  Caused by connection’s inconsistent QoS
Preventing delays, disorder, distortion
  Requires more dedicated bandwidth
  Requires techniques ensuring high QoS
QoS measures network service performance
  High QoS: uninterrupted, accurate, faithful reproduction
Improvements to QoS made in recent years
  Service quality now comparable to PSTN, cable TV
Notes: QoS (Quality of Service) Assurance
VoIP, video over IP transmission difficulty
  Caused by connection’s inconsistent QoS
Preventing delays, disorder, distortion
  Requires more dedicated bandwidth
  Requires techniques ensuring high QoS
QoS measures network service performance
  High QoS: uninterrupted, accurate, faithful reproduction
Improvements to QoS made in recent years
  Service quality now comparable to PSTN, cable TV

## Slide 56: DiffServ (Differentiated Service)
Addresses QoS issues through traffic prioritization
DiffServ
  Modifies actual IP datagram
  Accounts for all network traffic
Can assign different streams different priorities
To prioritize traffic
  IPv4 datagram: DiffServ field
  IPv6 datagram: Traffic Class field
Notes: DiffServ (Differentiated Service)
Addresses QoS issues through traffic prioritization
DiffServ
  Modifies actual IP datagram
  Accounts for all network traffic
Can assign different streams different priorities
To prioritize traffic
  IPv4 datagram: DiffServ field
  IPv6 datagram: Traffic Class field

## Slide 57: DiffServ (Differentiated Service)
Two forwarding types
  EF (Expedited Forwarding)
    Data stream assigned minimum departure rate
    Circumvents delays
  AF (Assured Forwarding)
    Data streams assigned different router resource levels
    Prioritizes data handling
    No guarantee of on time, in sequence packet arrival
Notes: DiffServ (Differentiated Service)
Two forwarding types
  EF (Expedited Forwarding)
    Data stream assigned minimum departure rate
    Circumvents delays
  AF (Assured Forwarding)
    Data streams assigned different router resource levels
    Prioritizes data handling
    No guarantee of on time, in sequence packet arrival

## Slide 58: MPLS (Multiprotocol Label Switching)
Modifies data streams at Network layer
Replaces IP datagram header with label:
  At first router data stream encounters
  Next router revises label
  Label contains packet forwarding information
Considers network congestion
Very fast forwarding
Destination IP address compared to routing tables
  Forward data to closest matching node
Notes: MPLS (Multiprotocol Label Switching)
Modifies data streams at Network layer
Replaces IP datagram header with label:
  At first router data stream encounters
  Next router revises label
  Label contains packet forwarding information
Considers network congestion
Very fast forwarding
Destination IP address compared to routing tables
  Forward data to closest matching node

## Slide 59: CoS (Class of Service)
CoS
  Refers to techniques performed at Layer 2 on Ethernet frames
  Most often used to route Ethernet traffic between VLANs
  Priority Code Point (PCP)
  A 3-bit field in the frame header of a frame that has been tagged (addressed to a specific VLAN)
CoS sets these bits to one of eight levels ranging from 0 to 7
Notes: CoS (Class of Service)
CoS
  Refers to techniques performed at Layer 2 on Ethernet frames
  Most often used to route Ethernet traffic between VLANs
  Priority Code Point (PCP)
  A 3-bit field in the frame header of a frame that has been tagged (addressed to a specific VLAN)
CoS sets these bits to one of eight levels ranging from 0 to 7

## Slide 60: Troubleshooting Network Integrity and Availability
Integrity
  assurance that a network’s programs, data, services, devices, and connections have not been altered
Availability
  How consistently and reliably a file or system can be accessed
Uptime
  Measure of time functioning normally between failures
  Linux or UNIX command
  Microsoft utility
Notes: Troubleshooting Network Integrity and Availability
Integrity
  assurance that a network’s programs, data, services, devices, and connections have not been altered
Availability
  How consistently and reliably a file or system can be accessed
Uptime
  Measure of time functioning normally between failures
  Linux or UNIX command
  Microsoft utility

## Slide 61: Troubleshooting Network Integrity and Availability
Notes: Troubleshooting Network Integrity and Availability

## Slide 62: General Guidelines
Allow only network administrators to create or modify NOS and application system files
Monitor the network for unauthorized access or changes
Record authorized system changes in a change management system
Install redundant components
Perform regular health checks on the network
Check system performance, error logs, and the system log book regularly
Notes: General Guidelines
Allow only network administrators to create or modify NOS and application system files
Monitor the network for unauthorized access or changes
Record authorized system changes in a change management system
Install redundant components
Perform regular health checks on the network
Check system performance, error logs, and the system log book regularly

## Slide 63: General Guidelines
Keep backups, system images, and emergency repair disks current and available
Implement and enforce security and disaster recovery policies
Notes: General Guidelines
Keep backups, system images, and emergency repair disks current and available
Implement and enforce security and disaster recovery policies

## Slide 64: Fault Tolerance
Capacity for system to continue performing
  Despite unexpected hardware, software malfunction
Failure
  Deviation from specified system performance level
    Given time period
Fault
  Malfunction of one system component
  Can result in failure
Fault-tolerant system goal
  Prevent faults from progressing to failures
Notes: Fault Tolerance
Capacity for system to continue performing
  Despite unexpected hardware, software malfunction
Failure
  Deviation from specified system performance level
    Given time period
Fault
  Malfunction of one system component
  Can result in failure
Fault-tolerant system goal
  Prevent faults from progressing to failures

## Slide 65: Devices and Interfaces
Redundancy
  Reduces the risk of lost functionality and potentially lost profits
  Disadvantage: cost
Redundancy scenario:
  A network design with many single points of failure (see Figure 9-16)
  Solution: create a network design that ensures full redundancy for all components (see Figure 9-17)
Notes: Devices and Interfaces
Redundancy
  Reduces the risk of lost functionality and potentially lost profits
  Disadvantage: cost
Redundancy scenario:
  A network design with many single points of failure (see Figure 9-16)
  Solution: create a network design that ensures full redundancy for all components (see Figure 9-17)

## Slide 66: Devices and Interfaces
Notes: Devices and Interfaces

## Slide 67: Devices and Interfaces
Failover capable or hot swappable components
  Desired for switches or routers supporting critical links
  Adds to device cost
  Hot spare is a component already installed in a device that can assume control at failure
  Cold spare is a component, not installed, but can be in the event of failure
Link aggregation (port bonding)
  Combination of multiple network interfaces to act as one logical interface
  Example: NIC teaming
Notes: Devices and Interfaces
Failover capable or hot swappable components
  Desired for switches or routers supporting critical links
  Adds to device cost
  Hot spare is a component already installed in a device that can assume control at failure
  Cold spare is a component, not installed, but can be in the event of failure
Link aggregation (port bonding)
  Combination of multiple network interfaces to act as one logical interface
  Example: NIC teaming

## Slide 68: Devices and Interfaces
Load balancing (content switching)
  Automatic traffic distribution over multiple components or links
  To optimize performance and fault tolerance
Switch Dependent Mode
  NIC teaming accomplished with a single switch
  Requires an intelligent switch
  Variety of this mode implements Link Aggregation Control Protocol (LACP)
Notes: Devices and Interfaces
Load balancing (content switching)
  Automatic traffic distribution over multiple components or links
  To optimize performance and fault tolerance
Switch Dependent Mode
  NIC teaming accomplished with a single switch
  Requires an intelligent switch
  Variety of this mode implements Link Aggregation Control Protocol (LACP)

## Slide 69: Devices and Interfaces
Notes: Devices and Interfaces

## Slide 70: Devices and Interfaces
NICS could be teamed to multiple switches using Switch Independent Mode
  Can be used with nonintelligent switches
Notes: Devices and Interfaces
NICS could be teamed to multiple switches using Switch Independent Mode
  Can be used with nonintelligent switches

## Slide 71: Naming and Addressing Services
Naming and addressing services
  Failure causes nearly all traffic to come to a halt
Solution: maintain redundant name servers
Notes: Naming and Addressing Services
Naming and addressing services
  Failure causes nearly all traffic to come to a halt
Solution: maintain redundant name servers

## Slide 72: Naming and Addressing Services
DNS can point to redundant locations for each host name
Round-robin DNS
  Enables load balancing between servers and increases fault tolerance
Load balancer
  Distributes traffic intelligently among multiple computers
Notes: Naming and Addressing Services
DNS can point to redundant locations for each host name
Round-robin DNS
  Enables load balancing between servers and increases fault tolerance
Load balancer
  Distributes traffic intelligently among multiple computers

## Slide 73: Naming and Addressing Services
CARP(Common Address Redundancy Protocol)
  Allows a pool of computers or interfaces to share one or more IP addresses
  Pool is known as a group of redundancy
In CARP
  One computer, acting as the master of the group, receives requests for an IP address
  Then parcels out the requests to one of several computers in a group
Notes: Naming and Addressing Services
CARP(Common Address Redundancy Protocol)
  Allows a pool of computers or interfaces to share one or more IP addresses
  Pool is known as a group of redundancy
In CARP
  One computer, acting as the master of the group, receives requests for an IP address
  Then parcels out the requests to one of several computers in a group

## Slide 74: Naming and Addressing Services
Notes: Naming and Addressing Services

## Slide 75: Data Backup
Backup
  Copies of data or program files
  Created for archiving, safekeeping
When creating a backup system, keep in mind:
  Use only proven and reliable backup software
  Verify backup hardware and software are compatible with network
  Make sure backup software uses data error-checking
  Verify that your backup storage media provides sufficient capacity
Notes: Data Backup
Backup
  Copies of data or program files
  Created for archiving, safekeeping
When creating a backup system, keep in mind:
  Use only proven and reliable backup software
  Verify backup hardware and software are compatible with network
  Make sure backup software uses data error-checking
  Verify that your backup storage media provides sufficient capacity

## Slide 76: Data Backup
When creating a backup system, keep in mind (cont’d):
  Be aware of how your backup process affects the system
  Be aware of the degree of manual intervention required to manage backups
  Make wise choices for storage media
  When storing data to hard drives, recognize that drives can be installed on computers on the LAN
  Keep backups secure
Notes: Data Backup
When creating a backup system, keep in mind (cont’d):
  Be aware of how your backup process affects the system
  Be aware of the degree of manual intervention required to manage backups
  Make wise choices for storage media
  When storing data to hard drives, recognize that drives can be installed on computers on the LAN
  Keep backups secure

## Slide 77: Data Backup
When creating a backup system, keep in mind (cont’d):
  Consider cloud backups
  Decide what to back up
  Plan what type of backup will be done
    Full, incremental, or differential backups
  Plan when backups will be done
  Develop a backup schedule
  Establish a regular schedule of verification
Notes: Data Backup
When creating a backup system, keep in mind (cont’d):
  Consider cloud backups
  Decide what to back up
  Plan what type of backup will be done
    Full, incremental, or differential backups
  Plan when backups will be done
  Develop a backup schedule
  Establish a regular schedule of verification

## Slide 78: Summary
Baseline measurements allow you to compare future performance increases or decreases caused by network changes or events with past network performance
In addition to internal policies, a network manager must consider state and federal regulations
The syslog protocol is a standard for generating, storing, and processing messages about system events
Effective utilization of interface system and event logs can help identify and prevent complications
Notes: Summary
Baseline measurements allow you to compare future performance increases or decreases caused by network changes or events with past network performance
In addition to internal policies, a network manager must consider state and federal regulations
The syslog protocol is a standard for generating, storing, and processing messages about system events
Effective utilization of interface system and event logs can help identify and prevent complications

## Slide 79: Summary
Traffic shaping involves manipulating characteristics of packets, data streams, or connections to manage the type and amount of traffic traversing a network
Caching is the local storage of frequently needed files that would otherwise be obtained externally
Ethernet networks and the Internet are the most common examples of packet-switched networks
In a unicast transmission, a single node issues a stream of data to one other node
Signaling protocols set up and manage sessions between clients
Notes: Summary
Traffic shaping involves manipulating characteristics of packets, data streams, or connections to manage the type and amount of traffic traversing a network
Caching is the local storage of frequently needed files that would otherwise be obtained externally
Ethernet networks and the Internet are the most common examples of packet-switched networks
In a unicast transmission, a single node issues a stream of data to one other node
Signaling protocols set up and manage sessions between clients

## Slide 80: Summary
On a VoIP, logical channels are identified as port numbers at each IP address
SIP is an Application layer signaling and control protocol for multiservice, packet-based networks
MGCP and Megaco are commonly used on multiservice networks that support a number of media gateways
UDP is preferred over TCP for real-time services, such as telephone conversations and videoconferences
Notes: Summary
On a VoIP, logical channels are identified as port numbers at each IP address
SIP is an Application layer signaling and control protocol for multiservice, packet-based networks
MGCP and Megaco are commonly used on multiservice networks that support a number of media gateways
UDP is preferred over TCP for real-time services, such as telephone conversations and videoconferences

## Slide 81: Summary
QoS is a measure of how well a network service matches its expected performance
MPLS can operate over Ethernet frames, but it is more often used with other Layer 2 protocols
One way to consider availability is by measuring a system or network’s uptime
Redundancy is intended to eliminate single points of failure
Link aggregation is the seamless combination of multiple network interfaces or ports to act as one logical interface
Notes: Summary
QoS is a measure of how well a network service matches its expected performance
MPLS can operate over Ethernet frames, but it is more often used with other Layer 2 protocols
One way to consider availability is by measuring a system or network’s uptime
Redundancy is intended to eliminate single points of failure
Link aggregation is the seamless combination of multiple network interfaces or ports to act as one logical interface